## Slide 1: TAM

## Slide 2: Actuator Controls
Port and Pin | Logic Value | Function
Port B, 2/3 | 1/0 | Lower platform
Port B, 2/3 | 0/1 | Raise Platform
Port B, 6 | 0 | Retract Piston
Port B, 6 | 1 | Extend Piston
Port B, 7 | 0 | Lower Height Sensor
Port B, 7 | 1 | Raise Height Sensor

## Slide 3: Input Pins
Port A Pin | Input | Logic
0 | Magnetic Sensor | 1 if sample is metal
1 | Sens samp | 1 if sample is detected on platform
2 | Color sensor | 
3 | Platform position | 1 if platform is lowered
4 | Sens ru | 1 if platform is raised
5 | Sens erdy | 1 if piston is retracted
6 | Height sensor position | 1 if lowered

## Slide 4: Flow Chart
Check for Sample
Read Colour
Read Metallic
Read Height
Compare against Settings
Reject Object
Read Time
Accept Object
Commit Values
To Queue

## Slide 5: Height Reading and Conversion
Taken in as 11-bit integer
20 samples taken and averaged
Bit shifted into 8.8 fixed point
Multiplied by an 8.8 scale factor
ADC value
shifted value
scale factor

## Slide 6: Multitasking
µCOS-II pre-emptive multitasking kernel

## Slide 7: MAIN
Initialise
  Variables
  TAM
  LCD
Starting 2 of 3 Tasks
Main.c
ButtonWatch
TAMRunner
MenuManager

## Slide 8: ButtonWatch
Start or Stop
Start TAM
Set Flag

## Slide 9: TAMRunner
Wait for an Object
Test the object
Check settings
Write to the queue
Check Flag

## Slide 10: MenuManger
Menus on LCD Screen
User Input
Read from queue
Output information

## Slide 11
ButtonWatch
TAMRunner
MenuManager
SETTINGS
QUEUE

## Slide 12
ButtonWatch
TAMRunner
MenuManager
SETTINGS
QUEUE
mutSettings
mutQueue